## Slide 1
http://xkcd.com/1134/

## Slide 2: Digital circuits
David Kauchak
CS52 – Fall 2015

## Slide 3: Admin
Assignment 4 due Monday at 11:59pm
Assignment 5 posted soon
  due Friday Oct. 23rd, at 5pm
CS lunch today!

## Slide 4: Midterm
Average: 23.25
Top quartile: 26
Top half (median): 24.6
Bottom quartile: 21.4

## Slide 5: Diving into your computer

## Slide 6: Normal computer user

## Slide 7: After intro CS

## Slide 8: After 5 weeks of cs52

## Slide 9: What now?

## Slide 10: One last note on CS41B
memory address
instructions (assembly code)
binary representation of code
How do we get this?

## Slide 11: Encoding assembly instructions
1001 0100 0000 0000
1001 1000 0000 0000
opcode
1100 1100 0000 0000
dest
src0
src1

## Slide 12: What now?
1001 0100 0000 0000
1001 1000 0000 0000
1100 1100 0000 0000

## Slide 13: Review: binary addition
01010
01111
?
Do the binary addition, making sure to keep track of the carries.
Assume unsigned numbers for now.
+

## Slide 14: Review: binary addition
01010
01111
11001
0
1
1
1
Just to be sure, what are these numbers in decimal?
+

## Slide 15: Review: binary addition
01010
01111
11001
0
1
1
1
10
15
25
We saw before, that we can view this problem recursively. How?
+

## Slide 17
handle a digit at a time
01010
01111
11001
0
1
1
1
+

## Slide 18
generate two pieces of information
output bit
carry bit
01010
01111
11001
0
1
1
1
+

## Slide 19: A recursive component
in1
in2
out
carry-out
carry-in
01010
01111
11001
0
1
1
1
+

## Slide 20: Adding with components
in1
in2
out
carry-out
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
01010
01111
0
1
1
1
0
1
1
1
+

## Slide 21: Adding with components
in1
in2
out
carry-out
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
01010
01111
0
1
1
1
0
1
1
1
?
?
+

## Slide 22: Adding with components
in1
in2
out
carry-out
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
01010
01111
0
1
1
1
0
1
1
1
?
?
1
1
0
0
+

## Slide 23: Adding with components
in1
in2
out
carry-out
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
01010
01111
0
1
1
1
0
1
1
1
?
?
1
1
0
0
1
0
0
1
+

## Slide 24: Adding with components
in1
in2
out
carry-out
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
01010
01111
0
1
1
1
0
1
1
1
?
?
1
1
0
0
1
0
0
1
1
0
0
1
+

## Slide 25: Adding with components
in1
in2
out
carry-out
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
in1
in2
out
carry-out
carry-in
01010
01111
0
1
1
1
0
1
1
1
1
1
0
0
1
0
0
1
1
0
0
1
1
1
1
1
1
+

## Slide 26: Implementing the component
in1
in2
out
carry-out
carry-in
What goes on inside the component?

## Slide 27: Implementing the component
in1
in2
out
carry-out
carry-in
Current implementation uses addition!

## Slide 28: Implementing the component
in1
in2
out
carry-out
carry-in
in1 | in2 | carry-in | out | carry-out
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
What are the outputs?

## Slide 29: Implementing the component
in1
in2
out
carry-out
carry-in
in1 | in2 | carry-in | out | carry-out
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1

## Slide 30: Another implementation
Don’t use addition anymore
Translated the problem into a boolean logic problem

## Slide 31: What are some boolean operators?
A | B | A and B | A or B | not A
0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 1 | 1
1 | 0 | 0 | 1 | 0
1 | 1 | 1 | 1 | 0

## Slide 32: What are some boolean operators?
A | B | A and B | A or B | not A | A nand B | A nor B | A xor B
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 33: Gates
Gates have inputs and outputs
  values are 0 or 1
Are hardware components!

## Slide 34: Gates as hardware

## Slide 35: Utilizing gates
1
0
0
?
A | B | A and B | A or B | not A | A nand B | A nor B | A xor B
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 36: Utilizing gates
1
0
0
0
0
A | B | A and B | A or B | not A | A nand B | A nor B | A xor B
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 37: Utilizing gates
1
1
1
?
A | B | A and B | A or B | not A | A nand B | A nor B | A xor B
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 38: Utilizing gates
1
1
1
0
0
When is this circuit 1?
A | B | A and B | A or B | not A | A nand B | A nor B | A xor B
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0

## Slide 39: Utilizing gates
1
1
1
in1 | in2 | in3 | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 0 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 0
1 | 1 | 1 | 0
Notes: nor is only true with inputs 0, 0
and gate will therefore only be true when in1 and in2 are both 0 and in3 is 1

## Slide 40: Designing more interesting circuits
in1 | in2 | in3 | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
A | B | A and B | A or B | not A | A nand B | A nor B | A xor B
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
Design a circuit for this

## Slide 41: Designing more interesting circuits
in1 | in2 | in3 | OUT
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 1
0 | 1 | 1 | 1
1 | 0 | 0 | 1
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1

## Slide 42: Back to addition…
in1
in2
out
carry-out
carry-in
in1 | in2 | carry-in | carry-out | sum
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 43: A half-adder: no carry-in
A | B | carry | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 44: A half-adder: no carry-in
A | B | A and B | A or B | not A | A nand B | A nor B | A xor B
0 | 0 | 0 | 0 | 1 | 1 | 1 | 0
0 | 1 | 0 | 1 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0 | 1 | 0 | 1
1 | 1 | 1 | 1 | 0 | 0 | 0 | 0
Design a circuit for this
Hint: solve each output bit independently
A | B | carry | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 45: A half-adder: no carry-in
low order bit of A+B
higher order bit of A+B
A | B | carry | sum
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 46: Implementing a full adder

## Slide 47: Implementing a full adder
low order bit of A+B
high order bit of A+B
low order bit of A+B+C
high order bit of A+B+C
Can I ever get a carry from both half adders?

## Slide 48: Implementing the component
in1
in2
out
carry-out
carry-in
What goes on inside the component?

## Slide 49: Implementing the component
A
B
sum
carry-out
carry-in

## Slide 50: Ripple carry adder
To implement an n-bit adder, we chain together n full- adders, each adder handles one bit position
A0
B0
out
carry-out
A1
B1
out
carry-out
carry-in
A2
B2
out
carry-out
carry-in
A3
B3
out
carry-out
carry-in
carry-in
A = A3 A2 A1 A0
B = B3 B2 B1 B0
Adder for adding 4-bit numbers
?

## Slide 51: Ripple carry adder
To implement an n-bit adder, we chain together n full- adders, each adder handles one bit position
A0
B0
out
carry-out
A1
B1
out
carry-out
carry-in
A2
B2
out
carry-out
carry-in
A3
B3
out
carry-out
carry-in
carry-in
A = A3 A2 A1 A0
B = B3 B2 B1 B0
Adder for adding 4-bit numbers
0

## Slide 52: Signed addition
0010
1110
?
Do the binary addition, making sure to keep track of the carries.
Assume signed numbers for now.
+

## Slide 53: Signed addition
0010
1110
0000
1110
Is that right?
What numbers are these?
throw away last carry bit
+

## Slide 54: Signed addition
0010
1110
0000
1110
2
-2
0
Ripple carry adder will work for signed and unsigned numbers
+

## Slide 55: Subtraction
0010
1110
-
We can solve this doing addition

## Slide 56: Subtraction
0010
1110
-
0010
0010
flip bits and add 1
0100
Do addition!

## Slide 57: Ripple carry adder/subtractor
FA
FA
FA
FA
FA
FA
FA
FA
D = 0: addition
D = 1: subtraction
Why does this work?

## Slide 58: Ripple carry adder/subtractor
If D = 0
  Carry in for first adder = 0
  Bi XOR 0 = Bi
If D = 1
  Carry in for first adder = 1 (+1 to sum)
  Bi XOR 1 = NOT Bi (flip all the bits of B)
FA
FA
FA
FA

## Slide 59: C, N, Z and V bits
In addition to the sum, we often also calculate some other useful information:
  C: carry out bit of the adder
  Z: 1 if the total result is zero, 0 otherwise
  N: sign bit of the result
  V: if there was “signed overflow”: the result cannot be represented with the number of bits we’re using
What are the cases where signed overflow can occur?

## Slide 60: V bit
V: if there was “signed overflow”: the result cannot be represented with the number of bits we’re using
Adding two positive numbers (too big positive)
Subtracting a negative number from a positive number (too big positive)
Adding two negative numbers (too big negative)
Subtracting a positive number from a negative number (too big negative)

## Slide 61: Detecting overflow
0011
0101
+
Add these (as signed numbers).
Does overflow occur?

## Slide 62: Detecting overflow
0011
0101
+
Yes. How do we detect it?
1000
111

## Slide 63: Detecting overflow
0011
0101
+
- Added two positive numbers and got a negative
- In general: if the sign bits are the same (of the numbers we end up adding), but the higher order bit of result is different = overflow
1000
111

## Slide 64: Detecting overflow
0011
1001
-
Subtract these (as signed numbers).
Does overflow occur?

## Slide 65: Detecting overflow
0011
1001
-
1010
000
Yes. How do we detect it?

## Slide 66: Detecting overflow
0011
1001
-
1010
000
- Subtracted a negative number from a positive, should have been positive
- In general: if the sign bits are the different (of the numbers we end up subtracting), but the higher order bit of result is different = overflow

## Slide 67: Detecting overflow
0011
1101
-
0110
100
- Subtracted a negative number from a positive
- In general: if the sign bits are the same (of the numbers we end up adding), but the higher order bit of result is different = overflow

## Slide 68: Python basics