## Slide 1: CS41B machine
David Kauchak CS 52 – Fall 2015

## Slide 2: Admin
Assignment 3
  due Monday at 11:59pm
  one small error in 5b (fast division) that’s been fixed
Midterm next Thursday in-class (10/1)
  Comprehensive 
  Closed books, notes, computers, etc.
  Except, may bring up to 2 pages of notes
  Practice problems posted
    Also some practice problems in the Intro SML reading
  Midterm review sessions Tuesday and Wednesday (Q&A session for midterm)

## Slide 3: Midterm topics
SML
recursion
math

## Slide 4: Midterm topics
Basic syntax
SML built-in types
Defining function
  pattern matching
Function type signatures
Recursion!
map
exceptions
Defining datatypes
addition, subtraction, multiplication manually and on list digits
Numbers in different bases
Binary number representation (first part of today’s lecture)
NOT CS41B material

## Slide 5: Binary number revisited
What number does 1001 represent in binary?
Depends!
Is it a signed number or unsigned?
If signed, what convention are we using?

## Slide 6: Twos complement
For a number with n digits high order bit represents -2n-1
unsigned
20
21
22
23
signed
(twos complement)
20
21
22
-23

## Slide 7: Twos complement
What number is it?
unsigned
20
21
22
23
signed
(twos complement)
20
21
22
-23
1
0
0
1
1
0
0
1
9
-7

## Slide 8: Twos complement
What number is it?
unsigned
20
21
22
23
signed
(twos complement)
20
21
22
-23
1
1
1
1
1
1
1
1
15
-1

## Slide 9: Twos complement
What number is it?
unsigned
20
21
22
23
signed
(twos complement)
20
21
22
-23
1
1
0
0
1
1
0
0
12
-4

## Slide 10: Twos complement
How many numbers can we represent with each approach using 4 bits?
unsigned
20
21
22
23
signed
(twos complement)
20
21
22
-23
16 (24) numbers, 0000, 0001, …., 1111
Doesn’t matter the representation!

## Slide 11: Twos complement
How many numbers can we represent with each approach using 32 bits?
unsigned
20
21
22
23
signed
(twos complement)
20
21
22
-23
232 ≈ 4 billion numbers

## Slide 12: Twos complement
What is the range of numbers we can represent for each approach?
unsigned
20
21
22
23
signed
(twos complement)
20
21
22
-23
unsigned: 0, 1, … 15
signed: -8, -7, …, 7

## Slide 13
binary representation | unsigned | 
0000 | 0 | 
0001 | 1 | 
0010 | ? | 
0011 |  | 
0100 |  | 
0101 |  | 
0110 |  | 
0111 |  | 
1000 |  | 
1001 |  | 
1010 |  | 
1011 |  | 
1100 |  | 
1101 |  | 
1110 |  | 
1111 |  | 

## Slide 14
binary representation | unsigned | twos complement
0000 | 0 | ?
0001 | 1 | 
0010 | 2 | 
0011 | 3 | 
0100 | 4 | 
0101 | 5 | 
0110 | 6 | 
0111 | 7 | 
1000 | 8 | 
1001 | 9 | 
1010 | 10 | 
1011 | 11 | 
1100 | 12 | 
1101 | 13 | 
1110 | 14 | 
1111 | 15 | 

## Slide 15
binary representation | unsigned | twos complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | ?
1001 | 9 | 
1010 | 10 | 
1011 | 11 | 
1100 | 12 | 
1101 | 13 | 
1110 | 14 | 
1111 | 15 | 

## Slide 16
binary representation | unsigned | twos complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | ?
1010 | 10 | 
1011 | 11 | 
1100 | 12 | 
1101 | 13 | 
1110 | 14 | 
1111 | 15 | 

## Slide 17
binary representation | unsigned | twos complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1

## Slide 18
binary representation | unsigned | twos complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
How can you tell if a number is negative?

## Slide 19
binary representation | unsigned | twos complement
0000 | 0 | 0
0001 | 1 | 1
0010 | 2 | 2
0011 | 3 | 3
0100 | 4 | 4
0101 | 5 | 5
0110 | 6 | 6
0111 | 7 | 7
1000 | 8 | -8
1001 | 9 | -7
1010 | 10 | -6
1011 | 11 | -5
1100 | 12 | -4
1101 | 13 | -3
1110 | 14 | -2
1111 | 15 | -1
High order bit!

## Slide 20: A two’s complement trick
You can also calculate the value of a negative number represented as twos complement as follows:
  Flip all of the bits (0  1 and 1 0)
  Add 1
  Resulting number is the magnitude of the original negative number
1101
0011
flip the bits
0010
-3
add 1

## Slide 21: A two’s complement trick
You can also calculate the value of a negative number represented as twos complement as follows:
  Flip all of the bits (0  1 and 1 0)
  Add 1
  Resulting number is the magnitude of the original negative number
1110
0010
flip the bits
0001
-2
add 1

## Slide 22: Addition with twos complement numbers
0001
0101
+
?

## Slide 23: Addition with twos complement numbers
0001
0101
+
0110
1

## Slide 24: Addition with twos complement numbers
0110
0101
+
?

## Slide 25: Addition with twos complement numbers
0110
0101
+
1011?
1

## Slide 26: Addition with twos complement numbers
0110
0101
+
1011?
1
6
5
11
Overflow! We cannot represent this number (it’s too large)

## Slide 27: Addition with twos complement numbers
0110
1101
+
?

## Slide 28: Addition with twos complement numbers
0110
1101
+
0011
1
1

## Slide 29: Addition with twos complement numbers
0110
1101
+
0011
1
1
6
-3
3
ignore the last carry

## Slide 30: Subtraction
Ideas?

## Slide 31: Subtraction
Negate the 2nd number (flip the bits and add 1)
Add them!

## Slide 32: A two’s complement trick
You can also calculate the value of a negative number represented as twos complement as follows:
  Flip all of the bits (0  1 and 1 0)
  Add 1
  Resulting number is the magnitude of the original negative number
Why does this work?

## Slide 33: A two’s complement trick
You can also calculate the value of a negative number represented as twos complement as follows:
  Flip all of the bits (0  1 and 1 0)
  Add 1
  Resulting number is the magnitude of the original negative number
1101 +
What is:
0010
?

## Slide 34: Hexadecimal numbers
Hexadecimal = base 16
What will be the digits?

## Slide 35: Hexadecimal numbers
Hexadecimal = base 16
Digits
0
1
2
…
9
a (10)
b (11)
c (12)
d (13)
e (14)
f (15)
What number is 1ad?

## Slide 36: Hexadecimal numbers
Hexadecimal = base 16
Digits
0
1
2
…
9
a (10)
b (11)
c (12)
d (13)
e (14)
f (15)
a d = 256+10*16+13=
= 429
160
161
162

## Slide 37: Hexadecimal numbers
Hexadecimal = base 16
Digits
0
1
2
…
9
a (10)
b (11)
c (12)
d (13)
e (14)
f (15)
Hexadecimal is common in CS.
Why?

## Slide 38: Hexadecimal numbers
Hexadecimal = base 16
Digits
0
1
2
…
9
a (10)
b (11)
c (12)
d (13)
e (14)
f (15)
Hexadecimal is common in CS.
4 bits = 1 hexadecimal digit
What is the following number in hex?
0110 1101 0101 0001

## Slide 39: Hexadecimal numbers
Hexadecimal = base 16
Digits
0
1
2
…
9
a (10)
b (11)
c (12)
d (13)
e (14)
f (15)
Hexadecimal is common in CS.
4 bits = 1 hexadecimal digit
What is the following number in hex?
0110 1101 0101 0001
6
d
5
1

## Slide 40: Computer internals

## Slide 41: Computer internals simplified
What does it stand for?
What does it do?
CPU
RAM
What does it stand for?
What does it do?

## Slide 42: Computer internals simplified
(Central Processing Unit,
aka “the processor”)
CPU
RAM
(Random Access Memory,
aka “memory” or “main memory”)
Does all the work!
Temporary storage

## Slide 43: Computer internals simplified
CPU
RAM
hard drive
“the computer”
Why do we need a hard drive?

## Slide 44: Computer internals simplified
CPU
RAM
hard drive
“the computer”
Persistent memory
RAM only stores data while it has power

## Slide 45: Computer simplified
hard drive
media drive
CPU
RAM
“the computer”
display
network
input devices

## Slide 46: Inside the CPU
CPU
processor
…
registers
processor: does the work
registers: local, fast memory slots
Why all these levels of memory?

## Slide 47: Memory speed
operation | access time | times slower than register access | for comparison…
register | 0.3 ns | 1 | 1 s
RAM | 120 ns | 400 | 6 min
Hard disk | 1ms | ~million | 1 month
google.com | 0.4s | ~billion | 30 years

## Slide 48: Memory
RAM
010101111000101000010010 …
What is a byte?
?

## Slide 49: Memory
RAM
01010111 10001010 00010010 …
byte = 8 bits
byte is abbreviated as B
My laptop has 16GB (gigabytes) of memory. How many bits is that?

## Slide 50: Memory sizes
 | bits
byte | 8
kilobyte (KB) | 2^10 bytes = ~8,000
megabyte (MB) | 2^20 =~ 8 million
gigabyte (GB) | 2^30 = ~8 billion
My laptop has 16GB (gigabytes) of memory. How many bits is that?

## Slide 51: Memory sizes
 | bits
byte | 8
kilobyte (KB) | 2^10 bytes = ~8,000
megabyte (MB) | 2^20 =~ 8 million
gigabyte (GB) | 2^30 = ~8 billion
~128 billion bits!

## Slide 52: Memory
RAM
01010111
10001010
00010010
01011010
…
Memory is byte addressable
address
0
1
2
3
…

## Slide 53: Memory
RAM
01010111
10001010
00010010
01011010
…
Memory is organized into “words”, which is the most common functional unit
address
0
1
2
3
…

## Slide 54: Memory
RAM
10101011 10001010 00010010 01011010
11001011 00001110 01010010 01010110
10111011 10010010 00000000 01110100
…
Most modern computers use 32-bit (4 byte) or 64-bit (8 byte) words
address
0
4
8
...
32-bit words

## Slide 55: Memory in the CS41B Machine
RAM
10101011 10001010
00010010 01011010
11001011 00001110
…
We’ll use 16-bit words for our model (the CS41B machine)
address
0
2
4
...
16-bit words

## Slide 56: CS41B machine
CPU
processor
registers
ic
r0
r1
r2
r3
instruction counter
(location in memory of the next
instruction in memory)
holds the value 0 (read only)
general purpose
read/write

## Slide 57: CS41B instructions
CPU
processor
registers
What types of operations might we want to do (think really basic)?

## Slide 59
operation name
(always three characters)

## Slide 60
operation arguments
R = register (e.g. r0)
S = signed number (byte)

## Slide 61
operation function
dest = first register
src0 = second register
src1 = third register
arg = number/argument

## Slide 62
add r1 r2 r3
What does this do?

## Slide 63
add r1 r2 r3
r1 = r2 + r3
Add contents of registers r2 and r3 and store the result in r1

## Slide 64
adc r2 r1 10
What does this do?

## Slide 65
adc r2 r1 10
r2 = r1 + 10
Add 10 to the contents of register r1 and store in r2

## Slide 66
adc r1 r0 8
neg r2 r1
sub r2 r1 r2
What number is in r2?

## Slide 67
adc r1 r0 8
neg r2 r1
sub r2 r1 r2
r1 = 8
r2 = -8, r1 = 8
r2 = 16